## Slide 1
Teachings for exercise 5b

## Slide 2: Statics of rigid bodies
You need to be able to solve problems about rigid bodies that are resting in equilibrium
If a body is resting in equilibrium:
There is no resultant force in any direction, so the horizontal and vertical forces sum to 0
The sum of moments about any point is 0 (the point does not have to be on the body itself)
5B

## Slide 3: Statics of rigid bodies
You need to be able to solve problems about rigid bodies that are resting in equilibrium
A uniform rod AB, of mass 6kg and length 4m, is smoothly hinged at A. A light inextensible string is attached to the rod at a point C where AC = 3m, and the point D, which is vertically above point A. If the string is keeping the rod in equilibrium in a horizontal position and the angle between the string and the rod is 40°, calculate:
The tension in the string
The magnitude and direction of the reaction at the hinge.
5B
A
B
C
D
3m
1m
T
40°
H
V
6g
40°
TSin40
TCos40
Start with a diagram and label on all the forces – split the tension into horizontal and vertical components
At the hinge there will be a vertical reaction and a horizontal reaction
Take moments about point A (as we have 3 unknown forces, 2 will be eliminated by doing this!)
These must be equal as the rod is in equilibrium
(1)
(2)
2m
(1)
(2)
Divide by 3Sin40
Calculate

## Slide 4: Statics of rigid bodies
You need to be able to solve problems about rigid bodies that are resting in equilibrium
A uniform rod AB, of mass 6kg and length 4m, is smoothly hinged at A. A light inextensible string is attached to the rod at a point C where AC = 3m, and the point D, which is vertically above point A. If the string is keeping the rod in equilibrium in a horizontal position and the angle between the string and the rod is 40°, calculate:
The tension in the string
The magnitude and direction of the reaction at the hinge.
5B
A
B
C
D
3m
1m
61
40°
H
V
6g
40°
61Sin40
61Cos40
Resolve Horizontally (set left and right forces equal to each other)
Resolve Vertically (set upwards and downwards forces equal to each other)
Calculate
Subtract 61Sin40
Calculate

## Slide 5: Statics of rigid bodies
You need to be able to solve problems about rigid bodies that are resting in equilibrium
A uniform rod AB, of mass 6kg and length 4m, is smoothly hinged at A. A light inextensible string is attached to the rod at a point C where AC = 3m, and the point D, which is vertically above point A. If the string is keeping the rod in equilibrium in a horizontal position and the angle between the string and the rod is 40°, calculate:
The tension in the string
The magnitude and direction of the reaction at the hinge.
5B
A
B
C
D
3m
1m
61
40°
H
V
6g
40°
61Sin40
61Cos40
H
V
A
H
V
A
R
The resultant force will be somewhere between V and H
 Use a right-angled triangle to help
46.72
19.6
Calculate
R

## Slide 6: Statics of rigid bodies
You need to be able to solve problems about rigid bodies that are resting in equilibrium
A uniform rod AB, of mass 6kg and length 4m, is smoothly hinged at A. A light inextensible string is attached to the rod at a point C where AC = 3m, and the point D, which is vertically above point A. If the string is keeping the rod in equilibrium in a horizontal position and the angle between the string and the rod is 40°, calculate:
The tension in the string
The magnitude and direction of the reaction at the hinge.
5B
A
B
C
D
3m
1m
61
40°
H
V
6g
40°
61Sin40
61Cos40
H
V
A
H
V
A
R
You also need to calculate the angle above the horizontal
46.72
19.6
Calculate
R
θ