## Slide 1
Teachings for
Exercise 2D

## Slide 2: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
Power is the rate of doing work
It is measured in Watts (W), where 1 watt = 1 joule per second
Often an engine’s power will be given in kilowatts (kW) where 1kW = 1000W
The power developed by an engine is given by the following formula:
P = power (W)
F = the driving force of the engine (N)
v = velocity (ms-1)
2D

## Slide 3: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
A truck is being pulled up a slope at a constant speed of 8ms-1 by a force of magnitude 2000N acting parallel to the direction of motion of the truck. Calculate the power developed in kilowatts.
Sub in values
Calculate
Change to kilowatts
2D

## Slide 4: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
A car of mass 1250kg is travelling along a horizontal road. The car’s engine is working at 24kW. The resistance to motion is constant and has magnitude 600N. Calculate:
The acceleration of the car when it is travelling at 6ms-1
The maximum speed of the car
Draw a diagram and show forces
T
600N
v = 6
P = 24000W
To calculate the acceleration we can use the formula F = ma. However, we do not know the driving force from the engine yet.
 We can calculate the driving force from the information given
Sub in values
Divide by 6
T is often used as the ‘tractive’ force of the engine
4000N
Resolve horizontally and sub in values
Calculate a
At a velocity of 6ms-1, the acceleration is 2.72ms-2
2D

## Slide 5: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
A car of mass 1250kg is travelling along a horizontal road. The car’s engine is working at 24kW. The resistance to motion is constant and has magnitude 600N. Calculate:
The acceleration of the car when it is travelling at 6ms-1
The maximum speed of the car
Draw a diagram and show forces
600N
When the car is at its maximum speed, the resultant force will be 0
The driving force must be 600N!
We can use this to calculate the velocity at this point…
4000N
600N
Sub in values
Calculate v
So the maximum speed of the car is 40ms-1
Important points to note:
As the velocity of the car increases, the driving force falls (it is harder for a car to accelerate more if it is already at a high speed)
This is the maximum speed for the given power level. It is possible to increase the power in an engine (for example by changing gear), and hence the top speed will increase
2D

## Slide 6: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
A car of mass 1100kg is travelling at a constant speed of 15ms-1 along a straight road which is inclined at 7˚ to the horizontal. The engine is working at a rate of 24kW.
Calculate the magnitude of the non-gravitational resistances to motion
The rate of working of the engine is now increased to 28kW. Assuming the resistances to motion are unchanged:
b) Calculate the initial acceleration of the car
7˚
7˚
1100g
1100gCos7
1100gSin7
R
T
N
As the speed is constant, the driving force must be equal to the forces opposing motion (gravity and anything else)
Find the driving force first
Sub in values
Calculate F
1600N
2D

## Slide 7: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
A car of mass 1100kg is travelling at a constant speed of 15ms-1 along a straight road which is inclined at 7˚ to the horizontal. The engine is working at a rate of 24kW.
Calculate the magnitude of the non-gravitational resistances to motion
The rate of working of the engine is now increased to 28kW. Assuming the resistances to motion are unchanged:
b) Calculate the initial acceleration of the car
7˚
7˚
1100g
1100gCos7
1100gSin7
R
N
As the speed is constant, the driving force must be equal to the forces opposing motion (gravity and anything else)
Now you have the driving force, resolve parallel to the plane
1600N
Sub in values. Remember acceleration is 0
Rearrange to find R
Calculate
268.2N
2D

## Slide 8: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
A car of mass 1100kg is travelling at a constant speed of 15ms-1 along a straight road which is inclined at 7˚ to the horizontal. The engine is working at a rate of 24kW.
Calculate the magnitude of the non-gravitational resistances to motion
The rate of working of the engine is now increased to 28kW. Assuming the resistances to motion are unchanged:
b) Calculate the initial acceleration of the car
7˚
7˚
1100g
1100gCos7
1100gSin7
N
As the speed is constant, the driving force must be equal to the forces opposing motion (gravity and anything else)
For part b), we need to start again by calculating the tractive force of the vehicle
1600N
268.2N
Sub in values
Calculate (remember to use the exact value later on)
1867N
2D

## Slide 9: Work, energy and power
You can calculate the power developed by an engine and solve problems about moving vehicles
A car of mass 1100kg is travelling at a constant speed of 15ms-1 along a straight road which is inclined at 7˚ to the horizontal. The engine is working at a rate of 24kW.
Calculate the magnitude of the non-gravitational resistances to motion
The rate of working of the engine is now increased to 28kW. Assuming the resistances to motion are unchanged:
b) Calculate the initial acceleration of the car
7˚
7˚
1100g
1100gCos7
1100gSin7
N
As the speed is constant, the driving force must be equal to the forces opposing motion (gravity and anything else)
Now use the F = ma formula again with the updated information…
268.2N
1867N
Sub in values
Divide by 1100
The initial acceleration will be 0.242ms-2
2D